DESCRIPTION

DEMOULD N is a water dilutable mould release agent for various types of moulding replication.

DEMOULD N is also used as an anti-stick agent for concrete truck shoots and areas where cement build up occurs.

DIRECTIONS: MOULD RELEASE AGENT

Apply DEMOULD N by brush, roller or spray at an approximate rate of 18-20m2/litre. The film should be thin with no runs. It is advisable to spray the mould at least two hours before pouring. This allows DEMOULD N to dry and establish before pouring cement mixes.

DIRECTIONS: ANTI STICK AGENT

Apply DEMOULD N by brush, roller or spray at an approximate rate of 8-10m2/litre. The film should be thin with no runs. Reapplication should occur daily or weekly. Tests should be carried out to evaluate suitability and reapplication rates.

All figures, spread rates and percentages are guides and tests should be performed to determine the correctness of the product for each individual use. In some cases, DEMOULD N can be diluted with water for mould release but extensive testing is required before use.

CLEAN UP

Clean up is done with water.

STORAGE

Store DEMOULD N in a cool area, between 5-30°C under cover and away from any other chemicals, foodstuffs or items.

PACK SIZES

DEMOULD N is sold in packs of 20 and 200 litres.

TRANSPORT

DEMOULD N is classified as a non-hazardous good for transport by Safe Work Australia.