DESCRIPTION

EXUTA LIQUID MASK (ELM) is a GLASS CLEAR PEELABLE Waterborne Protective Acrylic Membrane. EXUTA LIQUID MASK is applied to the glass and new aluminium frames in windows to give protection to the windows from building dust debris during the building process. After which, it is peeled off leaving a clean window glass and frame.

FEATURES

EXUTA LIQUID MASK forms a glass clear film allowing to view clearly through to what is on the other side of the glass pane.

EXUTA LIQUID MASK is able to be applied to other substrates, e.g. glazed ceramic tiles, smooth flat painted steel. The substrates need to be totally non-porous and smooth and very hard.

EXUTA LIQUID MASK is able to be used as a temporary water-resistant membrane.

PRECAUTIONS: EXUTA LIQUID MASK is best tested on a substrate required to be protected temporary to observe if the product is fit for the particular substrate.

APPLICATION

EXUTA LIQUID MASK can be applied by a long bristle brush, airless spray (low volume) or a lambs wool roller. Apply a thin film primer coat over the area to be coated. This will dry reasonably quickly. Apply a full coat over the primer at the required spread rate to give a finish glass clear dry film. Use the table following as a guide to the dry film thickness and wet film coverage necessary to achieve the dry film thickness. Usual application of the wet film is 2.0-2.5 m2/litre.

The wet film usually dries externally in summer conditions in 1.5 hours touch dry and up to 3 hours for touch dry in winter.  The film being wet does not inhibit applying coats to the surrounding surfaces where the ELM has been applied.

Full dry externally as a guide is 24-48 hours. Internally these times may be the same for similar weather conditions.

REMOVAL

Lift an edge of the coating using a fingernail or a square flat rectangular spatula can be pushed along the glass to the coating edge to lift and form a ridge which can be finger grasped to begin the pulling.

CLEAN UP

In the wet state clean off with a rag or water. In the dry state, peel off.

STORAGE

EXUTA LIQUID MASK is stored under cover with lid tightly pressed on between 5oC-30oC. If the product skins, the dried surface skin can be removed, and the liquid remainder used as normal.

SAFETY

EXUTA LIQUID MASK is neutral to slightly alkaline. Wear eye goggles, gloves and protective clothing when using or handling the product.

PACK SIZES

EXUTA LIQUID MASK is sold in containers of 5, 10, 15 litres.

TRANSPORT

EXUTA LIQUID MASK is not classified as dangerous or hazardous for transport by Safe Work Australia.